## Slide 1: Gen 2 Exadata Cloud at Customer
Deployment Details

## Slide 2: Gen 2 ExaCC Connectivity To Customer Network
Gen 2 ExaCC connects to customer network at OSI Network Layer 2
Each compute server offers 2 Client and 2 Backup Networks bonded in active-passive configuration
For Quarter Rack and larger systems, compute server offers physically separate backup and client networks copper or fiber connectivity
For Base System, compute server only offers physically separate backup and client network for fiber connectivity due to reduced hardware
Gen 2 requires outbound TCP/IP connectivity on port 443 from two local Control Plane servers to the nearest OCI Region
Control Plane servers connect with either copper or fiber networks

## Slide 3: Gen 2 ExaCC Connectivity To Customer Network
Customers will need maximum of 4 ports (2 for backup and 2 for client) per compute server to connect to their switches. In addition, customer will need four ports for VPN connectivity. The following table summarizes the port requirements customer will need to satisfy.
Size Of Rack | # Ports Client NW | # Ports Backup NW | Total # Ports
Base | 4 | 4 | 8
Quarter | 4 | 4 | 8
Half | 8 | 8 | 16
Full | 16 | 16 | 32
Control Plane | # Ports For VPN Connectivity to Oracle Public Cloud |  | Total # Ports
4 RJ45 or 4 SFP28 (2 per CP Server recommended, minimum 1 per CP server allowed) |  |  | 4 or 2

## Slide 4: Gen 2 ExaCC Connectivity To Customer Network
It is entirely up to the customer how they would like to connect to ExaCC. They can choose to connect both Client and Backup networks via the same switch, or they can have redundant switches for each of the two client and backup networks.
Each VM created in ExaCC must be assigned a Tag (VLAN ID) even if customer is choosing (or allowed) to create only one VM (it is not allowed to configure the connectivity as access VLANs) This is to ensure customer will be able to isolate subsequent VMs should they chose to create them later. Customer will need to configure these VLAN tags in their switches.

## Slide 5: Gen 2 ExaCC Client and Backup Networks IP Requirements
Recommend allocating large enough CIDR blocks to allow for future expansion when supported.
Elastic expansion is not supported in Gen 2 ExaCC version 1
Rack Size |  | CIDR size | Future Expansion Limit
Base, Quarter, Half | Recommended | /27 Client, /28 Backup | Full Rack (8 compute servers)
 | Minimum | /28 Client, /29 Backup | 5 compute servers
Full | Recommended | /26 Client, /27 Backup | 2x Full Racks (16 compute servers)
 | Minimum | /27 Client, /28 Backup | Full Rack (8 compute servers)

## Slide 6
ILOM
(1G NET MGT)
RJ45 (Net 1/2) OR SFP28 (Net1/2)
BCM57417 LOM
Motherboard Ports
eth1 eth2
eth4 eth3
2x QSFP+ QDR HCA
Infiniband
ib1 ib0
HOST admin
(1G NET 0)
eth0
eth5 eth6 eth7 eth8
KEY
10G RJ45 or 10/25G SFP28 Client
Backup – 10/25G SFP28
Backup – 1/10G RJ45
PN#7111181 - Oracle Quad Port 10GBase-T Adapter
(4x RJ45 10G Ports)
Fortpond (RJ45) Card
2x SFP28
10G/25G
BCM57414
Whitney (Fiber) Card
ExaCC X8-2 Compute Server – Quarter Rack or Larger
We ship 530-4449-01 - XCVR, 850NM, 1/10GBPS DUAL RA Short Range Transceivers Good Up To 100m for 10G transceiver selection in the SAR
If customer needs XVER SFP+28 25GBE SR FIBEROPTIC transceivers they must be ordered by the account team from iProcurement with destination address and contact as customer data center location. This limitation applies only till end of Nov 2019. After this date, it’ll be shipped from the factory. No cost to customer.
Client can only be on mother board. Backup interface must be of same type (copper or fiber) as client.

## Slide 7
ILOM
(1G NET MGT)
RJ45 (Net 1/2) OR SFP28 (Net1/2)
BCM57417 LOM
Motherboard Ports
eth1 eth2
eth4 eth3
2x QSFP+ QDR HCA
Infiniband
ib1 ib0
HOST admin
(1G NET 0)
eth0
KEY
10G RJ45 or 10/25G SFP28
Backup – 10/25G SFP28
2x SFP28
10G/25G
BCM57414
Whitney (Fiber) Card
Not expandable CPU1 is removed
ExaCC X8-2 Compute Server – Base System
We ship 530-4449-01 - XCVR, 850NM, 1/10GBPS DUAL RA Short Range Transceivers Good Up To 100m for 10G transceiver selection in the SAR
Client can only be on mother board. Backup interface must be Fiber if Client is Fiber. Backup can be shared copper or Whitney based Fiber if Client is copper interface.
If customer needs XVER SFP+28 25GBE SR FIBEROPTIC transceivers they must be ordered by the account team from iProcurement with destination address and contact as customer data center location. This limitation applies only till end of Nov 2019. After this date, it’ll be shipped from the factory. No cost to customer.

## Slide 8
ILOM
(1G NET MGT)
eth1 eth2
RJ45 (Net 1/2)
Motherboard Ports
eth4 eth3
2x QSFP+ QDR HCA
Infiniband
ib1 ib0
HOST admin
(1G NET 0)
eth0
KEY
10G RJ45 on motherboard OR
10/25G Fiber Ports on motherboard
2x SFP28
10G/25G
BCM57414
Whitney (Fiber) Card
Not expandable CPU1 is removed
ExaCC X8-2 – Control Plane Server
Ports To Use For VPN Connectivity to Oracle Public Cloud
The motherboard 10/25G SFP28 Ports have 530-4449-01 - XCVR, 850NM, 1/10GBPS DUAL RA Short Range Transceivers Good Up To 100m installed from the factory.
It is recommended to connect either both copper or both fiber ports to internet facing customer switch, however It is allowed to connect just one port per CP server as well.
If internet facing switch is copper, use copper eth 1 and eth2 on motherboard, if fiber, use fiber eth1 and eth2 on motherboard
If customer needs XVER SFP+28 25GBE SR FIBEROPTIC transceivers they must be ordered by the account team from iProcurement with destination address and contact as customer data center location. This limitation applies only till end of Nov 2019. After this date, it’ll be shipped from the factory. No cost to customer.

## Slide 9: Gen 2 ExaCC Client and Backup Networks Connectivity Matrix
ExaCC X8 Qtr and above (Fortpond is installed) |  | 
Client network | Client on Motherboard Copper | Client on Motherboard Fiber
Backup Network | Backup on Copper (Fortpond) | Backup on Fiber (Whitney)
ExaCC X8 Base (Fortpond is removed) |  | 
Client network | Client on Motherboard Copper | Client on Motherboard Fiber
Backup NW Option 1 | Backup on Shared Motherboard Copper | Backup on Shared Motherboard Fiber
Backup NW Option 2 | Backup on Fiber (Whitney) | Backup on Fiber (Whitney)

## Slide 10: Use the latest OECA for Key Data Sheet Values
Note: The above OECA link is internal. External link to OECA is here

## Slide 11: Deployment
Customer provides data center space, network drops, power drops, network configuration information, and IP addresses
  System will not ship until information is provided by customer
Then Oracle engineer comes onsite to:
  Deploy the ExaCC hardware and software
  Connect the system to your network
  Help customer to connect local control plane servers to public cloud control plane
  Help customer to add ExaCC system to their cloud account
Customer must enable OpenVPN connectivity from control plane servers in Exadata Rack to Oracle Public Cloud
Oracle will do an end-to-end validation of the system prior to handing over the system to the customer
Deployment takes about a week after engineer on site

## Slide 12: Exception Process
Typically approved exceptions after due diligence
  Reduced whips for PDUs
  Re-racking into customer rack
Exceptions can take time for approval. Start the process as soon as you learn any unique requirements from the customer
We review each request carefully before providing approval / denial
Use the link below for creating exception request
https://apex.oraclecorp.com/pls/apex/f?p=2839
(Note the above link is internal – Customers should work with their account teams if there is a need to file an exception)

## Slide 13: Deployment Checklist
Has the data center person responsible from customer team reviewed ExaCC Site Checklists and confirm that their DC fulfills these requirements for installation?
Has customer reviewed this PPT and agree to have the switches, cables and available ports ready to be connected to ExaCC machine?
Has customer reviewed and understood the control plane connectivity requirements and ready to provide Open VPN connectivity as described in this PPT?
Has customer reviewed and agree to fulfill environment requirements listed in a table at the end of Gen 2 ExaCC Datasheet
Customers: For any questions on any requirement listed in this guide, please work with your account team to address
Account Teams: For any questions on any requirement listed in this guide, please use the PM Contact list mentioned in the Deployment Checklist question on the SAR